## Slide 1
Notebook arc: what hardware can test
Notebooks 03–09 simulate the trade-off with circuit-level noise in Selene and Stim. Three predictions come out of the arc; all three rest on numbers no device has supplied yet.
NOTEBOOK 08, 09
Premise holds
Through detection events the full circuit looks like the paper's model: p_read flat in Δt, p_data = p_data(1) ⊕ p_idle
NOTEBOOK 09
Δt* from one calibration
Within +17–21% (d=3), +4–9% (d=5), ±2% (d=7). The model's p_L, though, is underestimated as d grows
NOTEBOOK 07, 07b, 09
Back to back at H2
At H2's estimated idle-to-gate ratio, waiting helps only at d=3, linear idle, by 11–16%
!
Never measured on a device: the idle rates γ (linear) and c (time²), how the time² term splits over time, whether idle error is Z only, and the round duration t_R.
Notebook arc on hardware · qec-timing · docs/notebook_arc_hardware_tests.md
1

## Slide 2
Six parameter groups, four never measured
Parameter | Used in | Current source
p1, p2 | 07–09 gate noise | H2-1E emulator sheet
p_meas (0→1, 1→0), p_init | 07–09 | H2-1E sheet, readout averaged
γ (linear idle) | 07–09 idle | Assumed: q(1) ≈ 1.1·p2
c (time² idle) and its split | 07–09 idle | Assumed; split unresolved
Idle X/Y part | 07 assumes 0 | Assumed: emulator's Z-only form
t_R, layers per round | 08, 09 time grid | Unknown
2
taken from a spec sheet
4
assumed or unknown
The assumed rows decide every H2 statement in 07–09. Calibrating them is the point of the hardware work.
Notebook arc on hardware · qec-timing · docs/notebook_arc_hardware_tests.md
2

## Slide 3
Blocker: no user-controlled delay
CHECKED 2026-10-12
Guppy 1.0.3 and 1.1.3: no sleep or delay; only barrier
Helios op set (tket-exts 0.14.3): RuntimeBarrier takes no duration
Selene experiment: barriers are removed before execution
Helios docs: "Runtime behavior is not specifiable by the user"
H2 / pytket-quantinuum 0.59.3: no documented sleep found
1
Ask Quantinuum
Delay on Helios or H2? An approved idle the compiler keeps? Does Nexus report duration?
2
Spectator idling
Target waits while k gate layers run on other qubits, ordered by barriers. Waits come in layer units
3
Hosted emulator first
It models idling by duration; local Selene doesn't. Validate the fallback there
Notebook arc on hardware · qec-timing · docs/notebook_arc_hardware_tests.md
3

## Slide 4
Fourteen testable claims, grouped by cost
No wait needed: run now
Low cost
T1 Readout flips only the record (03, 04d)
T2 Readout asymmetry 0→1 vs 1→0
T11 b_read ≈ 1 from gates alone (08, 09)
T13 CX compiles to 1 Rzz + 4 single-qubit gates (06a)
Single-qubit idle
Low–medium
T3 Idle error is Z only (07)
T4 Idle = linear γ + time² c (07)
T5 Does time² restart at gates? (09, open)
T6 H2 ratio q(1) ≈ 1.1·p2 (07 §7)
Spectator and small code
Medium, ~10⁴ shots
T7 Idling during neighbours' measurement (08, 09)
T8 Only X-basis memory sees idle error (07)
T9, T10 p_read flat; p_data = p_data(1) ⊕ p_idle
T12 Full-model decoder beats hand-built graph (06b)
Expensive: last
High, 10⁵+ per point
T14 Back to back best at H2; Δt* from one calibration (07 §7b, 09)
Predicted effect only 11–16% at d=3
Notebook arc on hardware · qec-timing · docs/notebook_arc_hardware_tests.md
4

## Slide 5
Order of work
0
Settle the delay question; get t_R Blocks T3–T10 and T14
1
No-wait tests T1, T2, T11, T13
2
Single-qubit idle T3 → T4 → T5, giving T6. Decides the H2 conclusions
3
Spectator idle T7: measurement crosstalk no notebook models
4
d=3 detection events T8 → T9, T10; T12 offline on the same shots
5
Conformance ladder Feed the calibrated parameters to each model, compare edges
6
Then decide on T14 Δt* and U depth in Stim first; spend p_L shots only if it pays
STEP 5: CONFORMANCE LADDER
07
Textbook gates, idle on data only
07b
+ native gates
08
+ uniform noise on every qubit
09
native + uniform
First rung that matches T9–T10 is sufficient.
Notebook arc on hardware · qec-timing · docs/notebook_arc_hardware_tests.md
5