## Slide 1
Stub to device
Running the stub's injected-noise surface-code memory on Quantinuum hardware.
Premise: ideal gates, X noise only, memory in |0_L⟩, Z-checks only. All noise is injected by one in-program RNG.
IDLE
p_idle = 1 − exp(−p·λ·Δt)
Grows with the wait between rounds
PER ROUND
p_data = 1 − (1−p)(1−p_idle)
One X draw per data qubit, before extraction
READOUT
p_read = b_read · p
Flips the record only: ancillas and final data
✓
Can show
The injected Δt trade-off reproduced on a device, on top of a Δt-independent background.
!
Cannot show
The device's own idle trade-off: Δt only changes a probability, the program never waits.
Stub to device · qec-timing · docs/stub_to_device.md
1

## Slide 2
What changes from emulator to device
 | Stub today (Selene, Stim backend) | Hardware version
Circuit | 1 ancilla, reused: checks run one after another | 1 ancilla per Z-check, CX in 4 layers, data → ancilla
Parameters | p_data, p_read, n_rounds passed to run() | Fixed at compile time: one program per sweep point
Native gates | CX → 1 Rzz + 4 single-qubit gates, noiseless | Same gates, now a real noise source
Randomness | RNG(base_seed + shot), verified in Selene | Unverified on hardware: test before anything else
Decoding | Weights from injected p_data, p_read | Weights = injected + measured background; same detector order; leaked shots flagged
Execution | emulator.run(), read with collate_tags() | Nexus submission, plus an adapter to the same reader
Stub to device · qec-timing · docs/stub_to_device.md
2

## Slide 3
Injected noise is not the only noise
1
Non-uniform
Data qubits get 1 or 2 CX per round; the model has one p_stab
2
Split
Gate errors on data act as p_stab; on ancillas, as extra p_read
3
Partial
Only the X/Y parts flip data in a Z-basis memory
4
Correlated
One Rzz fault can hit a data qubit and its ancilla together
Fix: compensate. Measure the background with zero injection, then lower the injected p_stab and p_read so the totals hit the target.
Δt is still not physical time: every round lasts the same on the device.
Chart: Right side of the U: R(n=3) / R_min
| 0 | 0.07 (H2) | 0.14 | 0.28 | 0.56
Uncompensated | 1.35 | 1.23 | 1.15 | 1.07 | 1.01
Compensated | 1.35 | 1.29 | 1.27 | 1.22
Stim model, d=5, T=10, p=0.015. Feasible: p2/p_inj ≲ 0.36 compensated, ≲ 0.15 uncompensated. At 0.56, compensation is impossible (background readout > p_read).
Stub to device · qec-timing · docs/stub_to_device.md
3

## Slide 4
Specification: rotated code, d = 3 and 5
Per round | d = 3 | d = 5
Qubits, (3d² − 1)/2 | 13 | 37
Rzz, 2d(d − 1) | 12 | 40
Ancilla measurements | 4 | 12
RNG draws | 13 | 37
Δt* (reference) | ≈ 2 | ≈ 1
Role | Smoke test | Experiment
Plus d² final data measurements. Both fit H2 (56 qubits); d=7 needs 73.
10
total time T
~20k
shots, d=5 grid
~9×10⁶
Rzz in total
Chart: d = 5 production grid: R / R_min
| 0.33 (30) | 0.71 (14) | 1.00 (10) | 1.43 (7) | 2.50 (4) | 3.33 (3)
d = 5 | 1.29 | 1.01 | 1 | 1.02 | 1.2 | 1.34
Reference path, injected noise only. ~3,000–3,600 shots per point for ±5% on R. The ends carry the U; the bottom is flat within 2%.
Stub to device · qec-timing · docs/stub_to_device.md
4

## Slide 5
What to run, and with which values
1
RNG check
Tiny job: random_float() and shot number per shot. Must vary.
2
Pre-hardware sim
Selene DepolarizingErrorModel at p2 = 1.05×10⁻³, p_meas ≈ 10⁻³
3
Background calibration
Zero injection, d = 5, a few round counts → p_stab_bg, p_read_bg
4
Reference rescan
Totals held at target; re-pick the grid if Δt* moved
5
d = 3 smoke test
A few points, end to end: submit, read, decode
6
d = 5 production
n = 30, 14, 10, 7, 4, 3 at ~3,000 shots each
RUN VALUES
p = 0.015, λ = 1, b_read = 1
T = 10, Δt = 10 / n
Keep p2 / p_inj ≤ 0.36 (≤ 0.15 if uncompensated). H2 sits at 0.07.
Don't lower p_inj below ~3×10⁻³ at H2's gate error.
Pinning Δt* (not just showing the U) needs ~4× shots on the middle points.
Stub to device · qec-timing · docs/stub_to_device.md
5